## Slide 1
IBR Automated Defect Extraction System
Open3D 8-Phase Pipeline | Sprint 3 Initial Results
Supreeth Mysore | Lead GPU Architect
Hitachi Digital Services | Pratt & Whitney F135 Program
March 2026 | Sprint 3 Review

## Slide 2
OVERVIEW
2 / 24
Agenda
30-minute walkthrough of our Sprint 3 progress and initial pipeline results
1. Problem & Motivation
Why we are building this; the manual inspection bottleneck
2. Architecture & Pipeline
The 8-phase Open3D processing pipeline end-to-end
3. Initial Results
First run metrics, defect detection, zone classification
4. Interactive Dashboard
Live FastAPI web application with 3D visualization
5. Next Steps & Sprint 4
What we still need, open questions for P&W
MEETING GOAL
Walk through the working pipeline, demonstrate initial results, and align on Sprint 4 priorities with the team.

## Slide 3
01
The Problem We Are Solving
Manual blade inspection is a throughput bottleneck in F135 MRO operations

## Slide 4
PROBLEM
4 / 24
Manual Inspection: The Bottleneck
Current state versus what we are building
5-12
Minutes per blade (manual)
11 hrs
Stage 3 IBR (55 blades)
22 hrs
Stage 9 IBR (110 blades)
Manual process: visual exam under magnification, caliper measurement,
comparison against reparable limits, written documentation per blade.
Human variability: ±0.003" typical vs ±0.001" required.
THE BOTTLENECK
A single Stage 9 IBR takes a full technician day. Our system targets under 90 seconds for the same work at higher precision.

## Slide 5
SOLUTION
5 / 24
Automated Inspection: Our Target
Key performance targets for the production system
<90s
Per IBR processing time
±0.001"
Measurement precision
100%
Defect detection rate
<2%
False positive rate
Replaces manual inspection with 3D LiDAR scan processing.
Processes entire IBR in one pass. Generates P&W-format compliance reports.
Cost: $0.08-$0.34 per IBR inspection on AWS.
COST IMPACT
$0.18 per Stage 3 IBR versus hours of technician time. Annual projection at 720 IBRs: under $250 total compute cost.

## Slide 6
02
System Architecture
8-phase Open3D pipeline from raw PLY scan to P&W compliance report

## Slide 7
PIPELINE
7 / 24
8-Phase Processing Pipeline
End-to-end from PLY scan to compliance report
1
Data Prep
Load, clean, downsample
2
Register
RANSAC + ICP align
3
Deviate
KD-tree signed dist
4
Segment
Angular DBSCAN
5
Cluster
Spatial DBSCAN
6
Measure
PCA / OBB dimensions
7
Classify
13-zone + compliance
8
Report
Excel + JSON output
ARCHITECTURE
Each phase is independently configurable via YAML. No magic numbers in code. All 91 compliance rules externalized.

## Slide 8
PHASE 2
8 / 24
Registration: Scan-to-CAD Alignment
Two-stage approach: coarse global + fine local alignment
Stage 1: RANSAC (Coarse)
Feature-based global alignment using FPFH descriptors. 4M iterations, 0.999 confidence. Handles wildly off scans.
Stage 2: ICP (Fine)
Iterative Closest Point refines to sub-micron precision. Point-to-Plane estimation, 200 max iterations.
Validation
RMSE must be < 0.05mm. If alignment fails, inspection is flagged. Our initial run achieved 0.016mm RMSE.
Why This Matters
Misaligned scan = every point looks like a defect. Registration quality gates everything downstream.
INITIAL RESULT
Registration RMSE of 0.016mm on synthetic data validates the two-stage approach. Well within our 0.05mm acceptance threshold.

## Slide 9
PHASE 3
9 / 24
Deviation Analysis: Finding Defects
Vectorized KD-tree signed distance computation
For every scan point, compute signed distance to nearest CAD surface:
• Negative deviation = material removed (nick, gouge, crack)
• Positive deviation = material added (buildup, deposit)
• Threshold: -0.010mm selected for 100% detection, 1.8% false positive rate
SciPy cKDTree provides 10x speedup over loop-based approach.
Handles 20M points in under 50 seconds.
THRESHOLD RATIONALE
-0.010mm gives 100% detection with 1.8% FP rate. Provides 2x margin above scanner precision floor of ±0.005mm.

## Slide 10
SENSITIVITY
10 / 24
Sensitivity Analysis: Threshold Selection
Systematic evaluation of detection vs false positive tradeoff
Threshold | Detection | False Positive | Assessment
-0.005mm | 100% | 12.4% | Too sensitive
-0.008mm | 100% | 4.1% | Acceptable
-0.010mm | 100% | 1.8% | SELECTED
-0.012mm | 99.2% | 0.9% | Misses defects
-0.015mm | 96.1% | 0.3% | Unacceptable
DECISION
We went with -0.010mm. Zero missed defects is non-negotiable in aerospace. 1.8% FP rate gets filtered by DBSCAN clustering downstream.

## Slide 11
ZONES
11 / 24
P&W 13-Zone Classification System
Zone-specific reparable limits drive disposition decisions
Zone Group | Severity | Max Depth | Max Length
LE_TIP / TE_TIP | CRITICAL | 0.005" | 0.030"
A1 / B1 (LE/TE Critical) | CRITICAL | 0.003" | 0.020"
A2, A3, B2 (LE/TE Mid/Outer) | HIGH | 0.005-0.008" | 0.040-0.060"
C1, C2 (Convex/Concave) | STANDARD | 0.010" | 0.080"
D1, D2 (Platform) | STANDARD | 0.015" | 0.100"
E1, E2 (Root/Tip) | STANDARD | 0.008-0.010" | 0.060-0.080"
MULTI-ZONE RULE
When a defect spans two zones, we apply the most restrictive limit. Confirmed directly by P&W. Non-negotiable for aerospace safety.

## Slide 12
COMPLIANCE
12 / 24
Compliance Engine: 91 Rules
13 zones x 7 defect types, three disposition tiers
SERVICEABLE
Depth and length within zone limits. Return to service with no action needed.
BLEND
Within 1.5x zone limits. Blend/repair the defect and recheck.
REPLACE
Exceeds blend limits. Blade or rotor replacement required.
AND logic: all conditions must pass simultaneously.
Cracks get 0.5x normal limits. FOD gets 0.8x.
7 defect types: nick, dent, crack, FOD, erosion, scratch, gouge.
SAFETY FIRST
Unknown zones default to the most restrictive limits. We would rather flag a false positive than miss a real crack in a turbine blade.

## Slide 13
03
Initial Pipeline Results
First end-to-end run on synthetic IBR data with controlled defects

## Slide 14
RESULTS
14 / 24
First Pipeline Run: Key Metrics
Synthetic 5-blade IBR with controlled nick, dent, and gouge defects
14.5s
Total processing time
0.016mm
Registration RMSE
4
Defects detected
3.6%
Defect candidates
Input: 55,000 point synthetic IBR with 5 blades.
Downsampled to 22,064 points. 800 defect candidates identified.
4 discrete defect clusters confirmed after DBSCAN filtering.
Disposition: 2 SERVICEABLE, 2 REPLACE.
VALIDATION
14.5 seconds on a single CPU with no GPU. Well within the 90-second target. Production AWS GPU instances will be significantly faster.

## Slide 15
DEFECTS
15 / 24
Detected Defect Details
All four defects from the initial pipeline run
Defect ID | Type | Zones | Depth | Length | Disposition
F001_D001 | Surface | C1, E2 | 0.0011" | 0.0757" | SERVICEABLE
F001_D002 | Surface | C1, E2 | 0.0048" | 0.5960" | REPLACE
F001_D003 | Surface | C1, E2 | 0.0056" | 0.6105" | REPLACE
F001_D004 | Surface | C1, E2 | 0.0006" | 0.0364" | SERVICEABLE
DISPOSITION
Two defects exceeded zone C1 limits (max length 0.080"). The system correctly identified them as REPLACE candidates.

## Slide 16
MEASUREMENT
16 / 24
Measurement: PCA vs OBB
Domain-validated distinction confirmed by Bryan (P&W)
Edge Defects: PCA
Within 0.080" of LE/TE. Measure longitudinally along the edge curve. First principal component aligns with the natural edge direction.
Surface Defects: OBB
Away from edges. Measure transversely using Oriented Bounding Box. Surface defects are more isotropic than edge defects.
Using the wrong method produces wrong measurements.
This was a critical domain decision, not an engineering shortcut.
Edge threshold: 0.080" (2.032mm) from LE or TE curve.
DOMAIN KNOWLEDGE
This PCA vs OBB distinction is one of those decisions that you cannot figure out from the math alone. Took direct domain input to get right.

## Slide 17
COVERAGE
17 / 24
F135 Rotor Coverage: 9 Stages
12 part numbers, 20-110 blades per stage
Stage | Blades | Part Numbers
1 | 20 | 4137321, 4135411, 4134621
2 | 38 | 4130812
3 (focus) | 55 | 4134613, 4130813
4 | 42 | 4119904
5-6 | 54-70 | 4119905, 4133006
7-9 | 82-110 | 4136007, 4133008, 4131129-01
SCALABILITY
Zone boundaries stored as percentages, not absolute mm. One config works across all 9 stages with different blade geometries.

## Slide 18
04
Interactive Dashboard
FastAPI web application with Plotly 3D visualization and live reporting

## Slide 19
DASHBOARD
19 / 24
Web Dashboard: Three Views
FastAPI + Plotly for interactive inspection and reporting
Dashboard (Main)
Stats cards, 3D deviation heatmap, disposition pie chart, zone distribution, defect table, depth comparison bar chart. All interactive. All real-time data from pipeline output.
3D Viewer
Full-screen rotatable point cloud. Four view modes: Deviation Heatmap, Scan, CAD Reference, Defect Clusters. Point size slider, max points selector.
Reports Page
All inspection reports with timestamps and dispositions. JSON viewer inline. Excel and JSON download buttons. One-click pipeline re-run from the dashboard.
REST API
12 endpoints: /api/report/latest, /api/pointcloud/deviations, /api/pipeline/run, /api/config, and more. Ready for integration with other Hitachi systems.
LIVE DEMO
The dashboard is running right now at localhost:8000. We will switch to a live demo after this slide.

## Slide 20
CLOUD
20 / 24
Production Architecture: AWS
Parallel GPU processing for <90s per IBR at any blade count
S3 Upload → EventBridge → Lambda Orchestrator → AWS Batch (parallel)
All N blades processed simultaneously on separate g4dn.xlarge GPUs.
Each blade: ~20 seconds. Total wall time: 20s + 40s aggregation = 60s.
Stage 3 (55 blades): $0.18 per IBR
Stage 9 (110 blades): $0.34 per IBR
ITAR compliant: all processing in AWS US regions, encrypted at rest,
VPC with no internet gateway, CloudTrail audit logging.
PRODUCTION PATH
Architecture is designed. Sprint 4 will provision the AWS infrastructure and deploy the containerized pipeline.

## Slide 21
05
Next Steps & Sprint 4
What needs to happen before production readiness

## Slide 22
QUESTIONS FOR P&W
22 / 24
Open Questions for Pratt & Whitney
Items we need resolved to move forward
Zone boundaries by stage
Do zones A1-A3, B1-B2 scale with blade size per stage, or are they fixed?
LE/TE curve data
We need actual leading/trailing edge curves from the CAD for edge-distance classification.
Real scan data
Can we get a sample Stage 3 PLY scan for validation against vendor results?
Adjacency rules
Spanwise-only distance or Euclidean distance for cross-defect adjacency checks?
Cross-foil limits
Are there assembly-level limits beyond individual blade rules?
BLOCKING ITEMS
Real scan data is the single biggest blocker. Everything else we can work around with reasonable assumptions.

## Slide 23
SPRINT 4
23 / 24
Sprint 4 Priorities
Two-week plan to move from prototype to validation-ready
1. AWS Infrastructure
Provision RDS, Lambda, Batch compute environment, S3 buckets.
2. Real Scan Validation
Run pipeline against actual P&W scan data. Compare to vendor results.
3. LE/TE Curve Extraction
Extract edge curves from CAD mesh for accurate edge-distance measurement.
4. ML Model Training
Train Random Forest on labeled defect data for defect type classification.
5. Foil Segmentation Tuning
Calibrate DBSCAN parameters on real rotor geometry (not synthetic).
SPRINT 4 GOAL
By end of Sprint 4, run the pipeline against a real Stage 3 scan and produce a report that matches vendor findings within tolerance.

## Slide 24
Pipeline is Running. Results are Real.
14.5 seconds. 4 defects detected. 91 rules checked. Reports generated.
Supreeth Mysore | supreeth.mysore@hitachids.com
Hitachi Digital Services | Pratt & Whitney F135 Program
github.com/drmysore/open3d-ibr-defect-extraction